|  | ......................... Pcs. .............................. € .............................. € MSW Classicline, Pureline, Protectline GEZE MSW Classic-, Pure- and Protectline manual sliding wall system consisting of glass panels which can be manually moved independently of each other, an aluminium track system, and a stacking area to park the panels which is dimensioned according to the number of panels in the system. Dimensions of the manual sliding wall Clear width: ............... mm Clear height: ............... mm (finished floor level to lower edge of ceiling max. 4000 mm) Number of panels: …. pcs. SmartGuide Enables the guiding side of the roller carriage in the track to be switched over without the use of an external control unit. This means that even complex track layouts can be realised while maintaining permanent guiding of the carriages. System layouts without swing door end panel allow the complete opening of the front of the system. Track system Smooth operation due to guided curve technology for easy operation of the panels, no sharp-angled or unguided branches. Carriage with permanently engaged guide rollers and mechanically coded track, either fixed or with auto-reversible guiding side, which makes it very simple to use and prevents maloperation. Carriages with plastic-coated, quiet-running track rollers and sealed ball bearings, but no spherical or gliding discs are permitted. Track consisting of extruded aluminium profiles with a cross-section of 96 x 66 mm. On-site ceiling end brackets are attached to the track by sliding blocks which can be supplied as an option. The track must be fixed to on site load-bearing components (e.g. steel structures or similar). Track layout ( ) straight ( ) continuously curved ( ) with ___ changes of direction in the front of the system ( ) according to the drawing attached Stacking area ( ) Position outside system front with vertical Comfort locking mechanism on last sliding panel ( ) Position inside system front with swing door end panel ( ) 90° stacking area (panels at 90° to the system's direction of operation) ( ) parallel stacking area (panels parallel to the system's direction of operation) ( ) custom-designed stacking area according to drawing ( ) with double track (recommended for visible stacking areas) ( ) with single track (recommended for invisible stacking areas) Locking to the floor Locking in double eccentric floor sockets with interchangeable insert for optimal adjustment and fit. Front side Comfort panel locking The panels are locked at the front using the MSW Comfort locking system, which locks securely into the floor sockets supplied and is also suitable for changing direction up to 15 degrees. The integrated activator unit connects the panels and prevents unauthorized levering. For stacking areas outside the system front, the last panel which is moved into the system front is equipped with a Comfort vertical lock. This locking mechanism closes the sliding panel by rotating the operating unit at 3 points simultaneously. The rotation mechanism can be locked via the integrated lock using a Euro profile cylinder. Alternative panel locking Alternatively, a version featuring arresting front floor locking and integrated floor locks with a Euro profile cylinder are available to lock the panels. Floor guide (as an option) ( ) with floor guide Panels Panels up to 1500 mm wide and 4000 mm high, weighing up to 150 kg. Upper and lower aluminium clamping profiles with replaceable clip-on cover. Upper and lower clamping profiles with integrated guide channels for securing the carriages, lockings and sealing components without additional add-on and connection profiles. Unbreakable end caps made of glass-fibre reinforced plastic. Carriages' adjustment range +4/-7 mm for subsequent height compensation, e.g. if ceiling sags. Single-piece, internally screwed glass clamping profile for dry glazing without glass machining for easy replacement of the glass panes if they are damaged. Design of cover profile (clip-on cover) ( ) Classicline (rounded styling, profile height 107 mm) ( ) Pureline (angular styling, profile height 110 mm) ( ) Protectline (angular styling, lower profile height 167 mm, upper 110 mm, improved glass protection) Surface of cover profile ( ) anodised EV1, silver-coloured ( ) anodised C31 similar to stainless steel ( ) powder-coated, colour in accordance with RAL Seal: ( ) on both sides, at the top ( ) on both sides, at the bottom Glass ( ) clear glass quality (low iron oxide content, no green tinge) ( ) ESG-H 10 mm (max. height 3000 mm) ( ) ESG-H 12 mm ( ) LSG made with ESG-H 10 mm (recommended max. height 3000 mm) ( ) LSG made with ESG-H 12 mm Subdivision of panels of the glass partition wall Locking by means of front side locking mechanisms or locking mechanisms which can be operated from the inside, depending on the installation position. Initial locking on the stacking area side carried out with bolt lock in the swing door end panel, or in the Comfort vertical locking mechanism for on-site Euro profile cylinders. …. pieces of sliding panels …. pieces of static swing door (on the stacking area) realised as ( ) single-action door with TS 3000 V ( ) swing door (no locking facility) ( ) double-action door with TS 550 NV floor spring ( ) with door handle set ( ) with push-bar on both sides …. pieces of sliding swing door with coupled locking for switching between sliding door and swing door function. The following versions can be selected: ( ) sliding swing door with TS 3000 V (limited opening direction (selectable inwards or outwards)) ( ) sliding swing door with GEZE Boxer (limited opening direction (selectable inwards or outwards)) ( ) sliding swing door (without locking facility) (limited opening direction (selectable inwards or outwards)) ( ) sliding swing door with TS 520 with swing function ( ) with door handle set ( ) with push-bar on both sides …. pieces of fixed panels |
| --- | --- |