|  | ......................... pcs. .............................. € .............................. € GEZE sliding fittings Levolan 120 SoftStop Sliding fittings for leaf weights up to 120 kg: - Clamping fittings for glass and wooden leaves, no leaf preparation necessary for installing the fittings - Smooth-running sliding fittings can be mounted from the front, tested in accordance with DIN EN 1527 and DIN EN 1670 - All fittings parts contained in the track with cover - Complete overall height of fittings only 50 mm - Height adjustable +/- 3 mm using ex-centric cam incl. removal protection - Installation compensation against building tolerances +/- 3° - For glass panes made of TSG 10, 12 mm and LSG 10.76 mm with LSG glue set - Corrosion-proof components - Only one track for wall or ceiling installation - Fixed panel, glass and recessed ceiling installation - bespoke, up to 6000 mm total track length Standard version (glass 1-leaf) wall / scope of supply: 1 track 1 cover profile 2 clamping roller carriages 6-8 cover brackets + 2 end stops 2 end covers for the track and cover profile 1 adjustable glass floor guide 8 – 13.5 mm Construction dimensions: Leaf width: ............ mm Glass thickness:........mm Colour: ( ) EV1 ( ) stainless steel optic ( ) acc. to RAL Track length ( ) 2450 mm ( ) 2850 mm ( ) Custom made, up to 6000 mm total track length Area of application: - For single or double-leaf sliding elements ( ) Levolan single-leaf for wall installation ( ) Levolan single-leaf for ceiling installation ( ) Levolan single-leaf for ceiling installation with fixed panel ( ) Levolan single-leaf for glass installation ( ) Levolan double-leaf for wall installation ( ) Levolan double-leaf for ceiling installation ( ) Levolan double-leaf for ceiling installation with fixed panel ( ) Levolan double-leaf for glass installation Accessories set Levolan 120 SoftStop: ( ) Left, damped on one side ( ) Right, damped on one side ( ) Damped on both sides |
| --- | --- |
| 1.1 | ......................... pcs. .............................. € .............................. € Floor guide Floor guide for glass leaf: ( ) Floor guide for glass leaf (stainless steel) for 8, 10, 12 mm glass ( ) Continuous floor guide for glass leaf Adjustable floor guide for glass leaf, individually variable at the range of 8 – 13,5 mm: ( ) Adjustable floor guide for glass leaf or floor guide for wooden leaf: ( ) Standard floor guide for wooden leaf |
| 1.2 | ......................... pcs. .............................. € .............................. € Additional buffer (floor or wall attachment) In addition to the end buffer, the door leaf must be stopped by a further buffer that is attached either at the middle of the door or at the bottom, so that the door leaf is stopped at the top and bottom at the same time. |