|  | ......................... pcs. .............................. € .............................. € GEZE sliding door fitting Perlan 140 Sliding door fitting for leaf weights up to 140 kg: - Closed aluminium track - Plastic roller carriage as well as maintenance-free ball bearings for smooth running. - Corrosion-proof components (protective class 2 in accordance with DIN EN 1670) Standard version/scope of supply: track for direct ceiling or wall installation using brackets, 2 roller carriages with suspension bolts, 2 suspension plates, 1 floor guide, 2 end stops with 1 hold-open spring Construction dimensions: Leaf width: ............ mm Type of installation: ( ) direct ceiling installation ( ) with wall attachment brackets ( ) optional ceiling installation with mounting plates Area of application: - single or multiple leaf sliding elements - vertical and wall offset adjustable |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Additional buffer (floor or wall mounting) In addition to the end stop, the door leaf must be stopped by a further buffer that is attached either at the middle of the door or at the bottom, so that the door leaf is stopped at the top and bottom at the same time. |
|  | ......................... pcs. .............................. € .............................. € Hold-open device ( ) Door hold-open device with spring ( ) Adjustable hold-open device |
|  | ......................... pcs. .............................. € .............................. € Continuous floor guide ( ) Single leaf wood/metal ( ) Single leaf glass ( ) Duosync version ( ) Telescope version |
|  | ......................... pcs. .............................. € .............................. € Accessories for glass sliding doors with glass clamping plate 30 mm Comprises 2 glass clamping plates incl. suspension bolt up to 80 kg leaf weight Glass thicknesses 8 – 12 mm (toughened safety glass) and 8.76 – 10.76 mm (laminated safety glass) Set available with individual covers for the glass clamping plates or continuous cover with end covers: ( ) Glass clamping plate set without cover ( ) Glass clamping plate set with cover EV1 ( ) Glass clamping plate set with cover in stainless steel optic ( ) Glass clamping plate set with cover RAL ( ) Glass clamping plate with continuous cover, length: .......... mm ( ) Set of end pieces, 2 pcs., for continuous cover Accessories for glass clamping plate 30 mm: ( ) Set end cover – EV1 ( ) Set end cover – stainless steel optic ( ) Set end cover – black ( ) Set end cover – RAL ( ) Cover profile for continuous cover length =6.0 m ( ) Cover profile for bespoke continuous cover EV1 ( ) Cover profile for bespoke continuous cover stainless steel optic ( ) Cover profile for bespoke continuous cover RAL To match these: floor guide for glass leaf ( ) Floor guide with variable adjustment for glass thicknesses 8 - 13.5 mm ( ) Floor guide for glass leaf (stainless steel) for glass thicknesses 8, 10, 12 mm |
|  | ......................... pcs. .............................. € .............................. € Accessories for glass sliding doors with glass clamping plate 45 mm Comprises 2 glass clamping plates incl. suspension bolt up to 140 kg leaf weight Glass thicknesses 8 – 12 mm (toughened safety glass) and 8.76 – 12.76 mm (laminated safety glass) Set available with individual covers for the glass clamping plates or continuous cover with end covers: ( ) Glass clamping plate set without cover ( ) Glass clamping plate set with cover EV1 ( ) Glass clamping plate set with cover in stainless steel optic ( ) Glass clamping plate set with cover RAL ( ) Glass clamping plate with continuous cover, length: .......... mm ( ) Set of end pieces, 2 pcs., for continuous cover Accessories for glass clamping plate 45 mm: ( ) Set end cover – EV1 ( ) Set end cover – stainless steel optic ( ) Set end cover – black ( ) Set end cover – RAL ( ) Cover profile for continuous cover length =6.0 m ( ) Cover profile for bespoke continuous cover EV1 ( ) Cover profile for bespoke continuous cover stainless steel optic ( ) Cover profile for bespoke continuous cover RAL To match these: floor guide for glass leaf ( ) Floor guide with variable adjustment for glass thicknesses 8 - 13.5 mm ( ) Floor guide for glass leaf (stainless steel) for glass thicknesses 8, 10, 12 mm |
|  | ......................... pcs. .............................. € .............................. € End caps black For covering the front-end of the track |
|  | ......................... pcs. .............................. € .............................. € Clip cover panel made of aluminium As a facing for the track and door suspension plate. To be attached directly on the track using panel fixing brackets (incl.). Colour: ( ) Anodised aluminium ( ) acc. to RAL ( ) for Perlan 140 with wall installation ( ) for Perlan 140 with ceiling installation ( ) side parts for wall or ceiling installation |
|  | ......................... pcs. .............................. € .............................. € Set Perlan AUT 2 For leaf weights up to 120 kg For automating a manual sliding door fitting. The motor is fixed directly to the track and is suitable for protected outdoor areas. The control unit is in the flush-mounted box of the control switch. Running speed max. 0.1 m/s. Not suitable for doors in passage areas. |
|  | ......................... pcs. .............................. € .............................. € Set Perlan 140 SoftStop For leaf weights up to 80 kg For soft braking and closing of the door. All functional parts are concealed invisibly in the track, so on-site facing is not required. Goes easy on the material, serves as pinch protection and ensures increased sliding comfort. Standard set contains: - 1 x Perlan 140 SoftStop roller carriage, for damping on one or both sides - 2 x buffers(incl. driver for the damper roller carriage) - 2 x standard suspension plate ( ) soft stop at one side ( ) soft stop at both sides Accessories: Perlan track, lowered ( ) bearing length approx. 6000 mm ( ) custom made, length: .......... mm |
|  | ......................... pcs. .............................. € .............................. € Set Perlan GGS Freely visible sliding door fitting made of stainless steel. Surfaces of all visible fitting components have been ground fine and matt in grit 600. For attachment to the Perlan 140 system. For glass doors and wooden doors. Set comprising 2 x Perlan GGS suspension rod incl. counter plate and fixing accessories. ( ) Set Perlan GGS - glass 8 - 12 mm and wood To match these: track Perlan 140 aluminium in stainless steel look ( ) bearing length approx. 6000 mm ( ) cut to length, length: .......... mm |
|  | ......................... pcs. .............................. € .............................. € Perlan 140 with fixed panel Fixed panel solution for Perlan 140. For fixed glass panels mounted on one or both sides. Enables an open and light room planning. Order specifications required: ( ) total width (wall opening) ( ) total height (wall opening) ( ) passage clearance width ( ) fixed panel width Optional order specifications: ( ) U profile at the side yes/no (standard: no) ( ) Offset Y for U profile bottom (standard: 40 mm) ( ) Offset Y for track profile (standard: 40 mm) ( ) Perlan 140 fixed panel 3 meter set: complete set for a 3-metre system: - 3 metres track Perlan 140 fixed panel - 1.5 metres cover profile - 4.5 metres U profile - 1 set end covers for U profile - 12 metres seals |
|  | ......................... pcs. .............................. € .............................. € Concealed wall bracket for Perlan 140 Concealed wall bracket for installation of the Perlan track in visible areas Order specifications required: ( ) length: .......... mm (with an total length of up to 6000 mm ) ( ) for glass leaves ( ) for wooden leaves (additional wall clearance 11 mm) Additional spacer profile for bridging frames or mirror tiles ( ) additional clearance 10 mm ( ) additional clearance 20 mm Accessories: ( ) Fastening by flat-head screws ( ) Fastening by countersunk-head screws (for Perlan SoftStop) ( ) Covers front side |
|  | ......................... pcs. .............................. € .............................. € GEZE modular fixed panel profile The GEZE fixed panel profile is suitable for bordering fanlights and side parts made of toughened safety glass and can be used as dry glazing for both internal and external applications. The system has been designed for glass thicknesses of 8, 10 and 12 mm. The glass thicknesses are fixed with the identical clamping unit, there is no need for the system to be changed. The threaded nuts for the clamping units contained in the system can be positioned freely in the basic profile and set to the glass edge in accordance with the TRPV (Technical rules for the Design and Construction of Point-Supported Glazing by the German Centre of Competence for Construction). Additional drill holes related to the glass edges or clamping units are not required. The glass panes are set using system-compliant adjusting units which are integrated in the clamping unit and make a tolerance compensation of +/- 2.5 mm possible. Construction components from other manufacturers are not approved for adjustment. In addition, the clamping units can be extended using a safety set for freely suspended glazing. The basic system can be combined with different design clip-on covers. Basic system / Basic profile ( ) Basic profile, aluminium, L = 6,000 mm ( ) Clamping system units, set 20 (20 pieces) adequate for a basic profile L = 6,000 mm, can be used for glass thicknesses of 10 and 12 mm Cover panels, design 40 aluminium (suitable for Patch Fittings, Perlan 140, Levolan etc.) ( ) Clip-on cover profile design 40 set for glass thicknesses of 8 to 12 mm (set = 2 profiles) ( ) Silver-coloured anodised surface ( ) Stainless steel colour anodised surface ( ) End cover cap for profile design 40 ( ) Silver-coloured anodised for glass thicknesses of 8 and 10 mm ( ) Silver-coloured anodised for glass thicknesses of 12 mm ( ) Stainless steel matt for glass thicknesses of 8 and 10 mm ( ) Stainless steel matt for glass thicknesses of 12 mm Cover design Pendulo ( ) Clip-on cover profile design Pendulo for glass thicknesses 8 and 10 mm (2 profiles necessary for 1 base profile) ( ) Silver-coloured anodised surface ( ) Stainless steel colour anodised surface ( ) End cover cap for profile design Pendulo ( ) Silver coloured painted for glass thickness 8 mm ( ) Silver coloured painted for glass thickness 10 mm ( ) Stainless steel optic painted for glass thickness 8 mm ( ) Stainless steel optic painted for glass thickness 10 mm Optional accessories for the modular fixed panel profile ( ) Additional clamping shims (set 40) for glass thicknesses of 8 mm ( ) Clamping system units, set 01 (1 piece) for additional clamping point ( ) Safety version set for fanlights and freely suspending glass panes, adequate for 5 clamping units |