|  | ......................... pcs. .............................. € .............................. € GEZE sliding door fitting Rollan 40 NT Sliding door fitting for leaf weights up to 40 kg: - Almost closed aluminium C-track - Double roller carriage, white, with plastic body and rollers as well as maintenance-free plain bearings for smooth running - Fitting tested in accordance with EN 1527 with corrosion protection according to EN 1670 Standard package / supplied by GEZE: Track for direct ceiling or wall installation using brackets, 2 double roller carriages with suspension bolts, 2 carrier plates, 1 floor guide for wooden leaves, 2 end buffers Construction dimensions: Leaf width: ............ mm Type of installation: ( ) Standard with wall attachment brackets and for direct ceiling installation ( ) Optional ceiling installation with fixing plates Area of application Single or multiple-leaf sliding elements adjustable height offset |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Additional buffer (floor or wall installation) In addition to the end buffer, another buffer is required to stop the door leaf; this buffer is installed either at the height of the centre of the door or below so that the door leaf is stopped above and below at the same time. |
|  | ......................... pcs. .............................. € .............................. € Accessories for glass sliding doors with glass clamping plate 30 mm: Comprises 2 glass clamping plates incl. suspension bolt up to 80 kg leaf weight Glass thicknesses 8 – 12 mm (toughened safety glass) and 8.76 – 10.76 mm (laminated safety glass) Set available with individual covers for the glass clamping plates or continuous cover with end covers: ( ) Glass clamping plate set without cover ( ) Glass clamping plate set with cover EV1 ( ) Glass clamping plate set with cover in stainless steel optic ( ) Glass clamping plate set with cover RAL ( ) Glass clamping plate with continuous cover, length: .......... mm ( ) Set of end pieces, 2 pcs., for continuous cover Accessories for glass clamping plate 30 mm: ( ) Set end cover – EV1 ( ) Set end cover – stainless steel optic ( ) Set end cover – black ( ) Set end cover – RAL ( ) Cover profile for continuous cover length =6.0 m ( ) Cover profile for bespoke continuous cover EV1 ( ) Cover profile for bespoke continuous cover stainless steel optic ( ) Cover profile for bespoke continuous cover RAL To match these: Glass floor guide ( ) Floor guide with variable adjustment for glass thicknesses 8 - 13.5 mm ( ) Stainless steel floor guide for glass thicknesses 8, 10, 12 mm |
|  | ......................... pcs. .............................. € .............................. € End buffer with hold-open spring For fixing the door in place on one side. |