|  | ......................... pcs. .............................. € .............................. € GEZE Electrically operated spindle drive E 350 N For daily aeration and ventilation as a direct opener on vertically installed or angled bottom-hung and top-hung casements as well as for light domes and skylights. Compact design spindle drive in 230 V version. Overload cut-off must be controlled electro-mechanically. Cables must be routed internally on the drive. Group actuation of a maximum of 10 drives in one group must be able to be implemented. Technical data: Tension and pressure: 750 N Current consumption: max. 0,4A, Enclosure rating: IP 65 Ambient temperature: -20° C to +70° C Stroke: ( ) Stroke 100 mm ( ) Stroke 150 mm ( ) Stroke 200 mm ( ) Stroke 230 mm ( ) Stroke 300 mm ( ) Stroke 500 mm ( ) Stroke 700 mm*) or ( ) Stroke 750 mm*) Special stroke 1000 mm possible on request. Version: Motor hood anodised aluminium EV1. Steel parts galvanised. Leaf width: ............ mm Casement height: ............ mm ( ) Vertically installed or angled bottom-hung or top-hung casements, outward opening ( ) Vertically installed bottom-hung or top-hung casements, inward opening *) In the case of angled casements, the stroke is limited to 500 mm. - Other strokes are possible for vertical casements on request |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € “Open-Stop-Close” selector switch ( ) Selector switch E 27, mounted flush to wall ( ) Selector switch E 33, for surface mounting Optional: ( ) Stroke limitation ( ) Position feedback to monitor final positions ( ) For use on large and heavy casements |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test by an expert authorised by the manufacturer. |
|  | ......................... pcs. .............................. € .............................. € Start-up and official approval Official approval of the complete smoke and heat extraction system by an officially recognised expert, who also hands over the acceptance certificates. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing of hold-open systems (optional position) Service package for maintenance and testing according to ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance and accident prevention inspection in accordance with ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable plan. Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection log. |