|  | ......................... pcs. .............................. € .............................. € GEZE TSA 325 NT: Revolving door system in 3 or 4-leaf version with freely selectable inside diameter up to 3600 mm, TÜV type-tested in accordance with DIN 18650, with fine frame in inviting light-coloured design, with different drive types and many possible configuration options Drive types ( ) Manual operation of the door. or ( ) Manually operated door with GEZE speed limiter, i.e. the max. speed of rotation of the revolving door is limited by a safety mechanism in the door. or ( ) Manually operated door with GEZE automatic positioning device, i.e. the manual door is moved by a motor at very low speed after passage to the initial position/end position. Safety concept: 1 x Emergency push button in accordance with DIN EN ISO 13850 or ( ) Semi-automatic GEZE Servo drive: Increased passage comfort compared with a manual door thanks to automatic starting of the turnstile. In order to reach walking speed, the turnstile can be overridden by hand. After the door has been passed, it revolves slowly to the end position. Complete drive with control on the interior, control in performance level "c" in accordance with DIN EN ISO 13849-1, convenient parameter setting, commissioning and after-sales service maintenance via optional Bluetooth connection to a PC, power supply: 230 V / 50 Hz / 350 W / 10 A Recommendation: Only if there is a constant range of users Safety concept: 1 x Emergency-stop button in accordance with DIN EN ISO 13850 or ( ) Fully automatic GEZE revolving door system (triggered via movement detector) Micro-processor controlled, electromechanical drive with infinitely adjustable speed, drive with two pre-set speeds. Complete drive with control on the interior, control in performance level "c" in accordance with DIN EN ISO 13849-1, convenient parameter setting, commissioning and after-sales service maintenance via optional Bluetooth connection to a PC, power supply: 230 V / 50 Hz / 350 W / 10 A, key programme switch for setting the operating modes. Fuse protection in accordance with DIN 18650 (TÜV type-tested and certified) comprising: - Post safety - Emergency push button in accordance with DIN EN ISO 13850 - Front post safety (non-contact) - Safety contact strip on the leaf, horizontal (heel protection) - Safety contact strip on the leaf, vertical (hand protection) - Coupled motion safety at the leaf (non-contact, from diameters > 3000 mm) Construction dimensions: ( ) Inside diameter: .................. ... mm (freely selectable between 1800 and 3600 mm) ( ) Outside diameter:.. ..................mm (freely selectable between 1880 and 3680 mm) ( ) Clear passage height DH: .... .. mm (up to 3000 mm, higher on request) ( ) Total height of door system: ...............mm ( ) Floor recess: ................ ..........mm (min. 60 mm) Note: Other dimensions on request. Door position: ( ) central ( ) off-centre, offset in relation to the façade ….. Model type: ( ) triple-leaf ( ) quadruple leaf Turnstile: ( ) rigid door leaf, fine-framed for mounting ESG glass. or ( ) hinged/swivelling leaf suitable for use in escape and rescue routes and for ventilation purposes with a canopy height of only 200 mm. Note: A suitable escape and rescue route is only achieved from an inside diameter of 2600 mm. Max. wind load 6 Beaufort. (only suitable for automatic doors) Note: Local building legislation must be complied with! Fine-framed drum walls made of GEZE aluminium profiles for mounting: ( ) Curved LSG 10 mm, clear or ( ) Curved thermally insulated panel lining 22 mm thick or ( ) Smooth-surface thermally insulated panels approx. 34 mm thick Aluminium ceiling construction: ( ) 200 mm standard height ( ) 75 mm for manual door and doors with underfloor operator ( ) 105 mm for the version with a waterproof roof or ( ) Raised ceiling canopy .............mm, with perimeter canopy cover made of curved aluminium sheets Roof covering outside: ( ) As a dust-proof roof with wooden board or ( ) Metal cover plate or ( ) Waterproof roof with 2 water spouts (flat roof without gradient) Roof covering inside: ( ) As a dust-proof roof with wooden board or ( ) Metal cover plate Soffit: ( ) Consisting of aluminium circle elements in system colour incl. inspection opening Surface of the light alloy parts: ( ) Powder coating according to RAL or ( ) LM anodised E6/EV1 or ( ) Colour anodised ............ or ( ) Coated with ground stainless steel, grain 240 or ( ) Coated with polished stainless steel Floor ring ( ) GEZE 360° stainless steel (V2A) floor ring made of rectangular tubing 30x30x2 mm. The floor ring is used as the floor covering edging at the same time. ( ) Sheet metal base 100 mm and/or ( ) Swivel flange (30x5 mm) or ( ) Direct installation of the self-supporting drum construction to the top edge of the finished floor. Note: Only possible with sufficient load-bearing and plane finished floor. Not possible for versions with hinged/swivelling leaves. Note: The insulation of the building is a contracted service and must be carried out on site. Floor cover ( ) GEZE clean scraping mat, anthracite colour, 22 mm, more colours available on request! or ( ) Floor cover to be carried out on site Delivery and installation Wiring to be carried out on site according to the GEZE cable plan by an electrical contractor. Installation, commissioning and instruction of the operator as well as documentation handover in compliance with DIN 18650 / EN 16005 through plant fitters or service partner. In compliance with DIN 18650 / EN 16005: - Safety analysis must be carried out as a basis for planning and execution - An inspection must be carried out at least 1 x year and after-sales service maintenance at least 1 x year |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Night-time closer (optional position) ( ) GEZE night-time closer sliding doors running on the outside, manual, closing possible from the inside and outside. For revolving doors with 70 mm canopy height and 4-leaf version only possible up to a max. inside diameter of 3000 mm. ( ) fine-framed in VSG 10 mm, clear or ( ) with aluminium panels Locking of the night-time closer sliding doors using: ( ) hook bolt lock (deadbolt monitoring not possible) or ( ) lever lock up Locking monitoring (deadbolt contact) or ( ) GEZE night-time closer sliding doors automated, non-retractable, with dead man’s control and rechargeable battery pack for emergency opening in the event of a power failure, 200 mm canopy height ( ) End position monitoring for night-time closer sliding doors Inside running manual night-time closer on request. |
|  | ......................... pcs. .............................. € .............................. € Locking (optional position) ( ) without locking mechanism or ( ) manual locking using GEZE extended bolt lock in the door leaf, inclusive profile half cylinder or ( ) electromechanical locking (bi-stable), in the event of a power failure the door remains in the state it was in prior to the power failure (automatic version only). Canopy height at least 75 mm Note: When using sliding doors with night-time closers, the turnstile does not need to be locked. |
|  | ......................... pcs. .............................. € .............................. € Handles (optional position) ( ) ground, vertical stainless steel push bars, dia. 30 mm, installation directly on the glass or ( ) ground, horizontal stainless steel push bars, dia. 30 mm, installation directly on the glass |
|  | ......................... pcs. .............................. € .............................. € Operation (optional position) GEZE key switch to “lock” the programme switch to prevent unauthorised changing of the operating mode, IP rating IP 40 ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Disabled person's button (optional position) ( ) Delivery and mounting of two GEZE push buttons with wheelchair symbol in the immediate entry area of the revolving door. When this push button is actuated, the revolving speed is reduced to an adjustable value to allow disabled persons a higher degree of access convenience and more safety. The activation duration can also be adjusted. Empty pipes must be routed to the installation point on site. Note: Can only be used with fully automatic version. |
|  | ......................... pcs. .............................. € .............................. € Lighting (optional position) ( ) ..... pcs. LED spotlight (max. 1 W per light) integrated in the soffit or ( ) ..... pcs. recess for lighting to be installed on site (diameter = ..... mm) |
|  | ......................... pcs. .............................. € .............................. € Underfloor operator (alternative position) ( ) GEZE drive as underfloor operator, box size of the drive in the floor: 720 x 1430 x 280 mm, prepared for on-site drainage, canopy height: 75 mm, floor recess min. 300 mm. Can be used with all drive types. |
|  | ......................... pcs. .............................. € .............................. € Hot-air curtain system (optional position) ( ) integrated in the suspended ceiling construction of the revolving door incl. blow-out channel in the canopy area. Minimum canopy height 400 to 600 mm, depending on diameter. Hot-air curtain system design with: ( ) Electric connection: Heat output: ............kW/ Amount of air.........m³/h ( ) Hot water connection Heat output: ............kW/ Amount of air.........m³/h Note: The power of the hot-air curtain equipment included in the offer has not been calculated by us; the dimensioning and specification of the hot-air curtains must be carried out by the specialist planner responsible. |
|  | ......................... pcs. .............................. € .............................. € Façade connection ( ) GEZE 34 mm panel ( ) installed on site with GEZE side connection profile |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing (option) Service package for maintenance and inspection in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years e.g. GEZE compact service package |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to EUR 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - exclusive package Service maintenance (optional position) Exclusive service package for servicing, maintenance in accordance with DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 60 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Complete repair: no separate charging for repairs (parts and working hours) and travel costs during the contract run time - Online access for the client to the project and system data at the contractor’s - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 5 years |