|  | GEZE glass fitting all-glass system GEZE all-glass fittings for the creation of all-glass walls for transparent spatial partitions consisting of single or double-leaf double-action doors with or without fanlight as well as fixed panels (side panels). The all-glass fittings consist of base rails screwed together in order to prevent unauthorised dismantling and of the corresponding functional units. The clip-on covers cover the base rail at the visible sides. The side panels must be framed with the modular fixed panel profile. This must be done at least at the horizontal and optionally at the vertical glass edges for fastening at the flanking structure. The profile is suitable for glass thicknesses of 10 and 12 mm. The system doesn’t need to be when the glass thickness changes. The clamping units that can be variably positioned in the basic profile enable alignment to the glass edge. Adjusting devices that allow a tolerance compensation of +/- 2.5 mm and improve the alignment of the glass panes with respect to one another are integrated into the clamping units. No construction components alien to the system are needed. Moreover, the clamping system can be extended by a security set for fanlights or freely suspended glazing without changing the clamping system. Fitting surface: ( ) Satin stainless steel ( ) Polished stainless steel Glass: ( ) 10 mm toughened safety glass, green glass ( ) 10 mm toughened safety glass, white glass ( ) 12 mm toughened safety glass, green glass ( ) 12 mm toughened safety glass, white glass |
| --- | --- |
|  | Corner patches: ( ) Lower corner fitting PT 10 with insert for flat conical spindle (e.g. floor spring GEZE TS 500 NV, TS 550 N) ......................... pcs. .............................. € .............................. € ( ) Upper corner fitting PT 20 with plastic bushing for 15 mm diameter pin ......................... pcs. .............................. € .............................. € ( ) Upper pivot PT 24 with 15 mm diameter round bolt (= standard surface installation) ......................... pcs. .............................. € .............................. € ( ) Top pivot bearing bracket PT 21 with easily rotating bolt (alternative to embedding in the masonry) ......................... pcs. .............................. € .............................. € ( ) Floor bearing (standard with flat conical spindle) ......................... pcs. .............................. € .............................. € |
|  | Fanlight and connector fittings: ( ) Fanlight fitting PT 30 with 15 mm pin and wall fixing accessories ......................... pcs. .............................. € .............................. € ( ) Angle fanlight fitting PT 40 with 15 mm pin for application with fixed side panel ......................... pcs. .............................. € .............................. € ( ) Connector patch PT 63 for fanlight and side panel, with stop for single-action doors ......................... pcs. .............................. € .............................. € ( ) Connector patch PT 84 glass-wall/glass-ceiling (twofold) ......................... pcs. .............................. € .............................. € ( ) Connector patch PT 90 glass-wall/glass-ceiling (simplex) ......................... pcs. .............................. € .............................. € |
|  | Patch locks and strike boxes: ( ) Center patch lock US 50 RD with round bolt ......................... pcs. .............................. € .............................. € ( ) Center patch lock US 50 with square bolt ......................... pcs. .............................. € .............................. € ( ) Corner patch lock PL 50 RD with round bolt ......................... pcs. .............................. € .............................. € ( ) Corner patch lock PL 50 with square bolt ......................... pcs. .............................. € .............................. € ( ) Bottom lock PL 55 with round bolt ......................... pcs. .............................. € .............................. € ( ) Single strike box GK 50 for center patch lock ......................... pcs. .............................. € .............................. € ( ) Double fanlight strike box GK 20 for two corner patch locks ......................... pcs. .............................. € .............................. € |
|  | Further accessories: ( ) GEZE TS 500 NV door closer (floor spring) ......................... pcs. .............................. € .............................. € ( ) GEZE TS 550 NV door closer (floor spring) ......................... pcs. .............................. € .............................. € ( ) Round bolt strike for patch locks with round bolts ......................... pcs. .............................. € .............................. € ( ) Square bolt strike for patch locks with square bolts ......................... pcs. .............................. € .............................. € |