|  | ......................... pcs. .............................. € .............................. € GEZE electric linear drive E 212 For daily aeration and ventilation and the safe and fast smoke dissipation at vertically installed, inwards opening skylight systems on bottom-hung, top-hung, side-hung, turn casements or louvre windows. Electric linear drive in 230 V or 24 V version. The stroke can be adjusted mechanically between 42 and 66 mm using limit switches. Drive can be used left / right and concealed / supported. Technical data: Stroke: 42 – 66 mm Connection voltage: 230 V AC/24 V DC Tension and pressure: 1400 N Current consumption: - E 212 R1= 0.4A - E 212 R = 0.4A - E 212/24 V DC = 1.2A Enclosed rating: IP 52 Temperature range –20°C to +70°C Dimensions: 210 x 33 x 80 mm Connection rod 8 mm ( ) E 212 R1/230 V AC With 1 relay for group switching via 1 operating spot/switch ( ) E 212 R/230 V AC With 2 relays for group switching via several operating spots/push button control ( ) E 212/24 V DC DC drive for 24V DC control units, including emergency power control units, suitable for RWA application Mechanical connection: ( ) supported rod connection on louvre lever ( ) concealed connection via driver to the louvre mechanism Drive installation: vertical at the side Space required: min. 35 mm Colour of cover hood: ( ) silver-coloured EV1 ( ) white, 9016 ( ) RAL shade according to choice |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Vent switch AS 500, for E 212 R ( ) with function buttons OPEN-STOP-CLOSE, for flush mounting ( ) optional surface mounting box |
|  | ......................... pcs. .............................. € .............................. € Fan switch AS 500, for E 212 R1 ( ) with function buttons OPEN-CLOSE, for flush mounting* |
|  | ......................... pcs. .............................. € .............................. € Vent switch AS 500, for E 212/24 V DC ( ) with function buttons OPEN-STOP-CLOSE, for flush mounting* * alternatively, for surface mounting, please use surface-mounting box (ID 120503). |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test by an expert authorised by the manufacturer. |
|  | ......................... pcs. .............................. € .............................. € Start-up and official approval Official approval of the complete smoke and heat extraction system by an officially recognised expert, who also hands over the acceptance certificates. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing of hold-open systems (optional position) Service package for maintenance and testing according to ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance and accident prevention inspection in accordance with ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable plan. Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection log. |