|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer system TS 5000 L-ISM VPK, in accordance with EN 1158, for general use on double leaf full panic doors with an X dimension up to 125 mm, size 2 – 6, with continuous guide rail BG 30 mm overall height, with integrated mechanical closing sequence control, vandalism protection against wilful maloperation of the closing sequence control, closing speed, back check and latching action, with visual closing force display, door leaf installation on opposite hinge side, with mounting plate. Colour: ( ) silver-coloured ( ) white ( ) acc. to RAL Accessories: ( ) Integrated almost invisible flexible opening restrictor for E/R/ISM guide rails Note: Use of a small inconspicuous carry bar often possible. The TS 5000 L-ISM VPK version is especially suitable for highly insulated door systems, door opening angle at X dimension 100 mm > 120° possible |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is infinitely variable adjustable (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |
|  | ......................... pcs. .............................. € .............................. € GEZE hold-open magnets, Operating voltage 24 V DC, Power consumption 1.5 W Retention force 490 N ( ) Hold-open magnet basic model (zinc plated without base plate) for in-wall installation or installation in any construction ( ) Hold-open magnet for wall mounting with base plate ( ) Hold-open magnet for flush-mounted installation ( ) Hold-open magnet for surface installation ( ) Base for hold-open magnet surface-mounted for floor installation ( ) Hold-open magnet with spacer tube zinc plated for floor/ceiling/wall mounting with swivelling magnetic head ( ) Version in basic length 185 mm ( ) Version in basic length 335 mm ( ) Hold-open magnet wall mounting, basic length 65 mm GEZE Magnetic counter plates, ( ) Standard magnetic counter plate on mounting plate with spring system for flatness with hold-open magnet ( ) Magnetic counter plate with spring buffer on installation housing with damping spring for soft spring buffer for heavy doors ( ) Magnetic counter plate, swivelling on mounting plate with swivelling magnetic counter plate for angle positions between door and hold-open magnet |
|  | ......................... pcs. .............................. € .............................. € GEZE current interruption switch (compulsory for hold-open magnets and freeswing function) ( ) Surface-mounted ( ) Flush-mounted |