|  | ......................... pcs. .............................. € .............................. € Integrated door closer system GEZE Boxer ISM with mechanical hold-open device, for double leaf doors; closing force size 2 – 4 in accordance with EN 1154; for single-action doors from 40 mm door leaf thickness, guide rail with integrated mechanical closing sequence control in accordance with EN 1158. Hold-open position can be overridden, vandalism protection against wilful maloperation of the closing sequence control, closing force, closing speed, hydraulic back check and latching action are adjustable after installation. When used on fire and smoke protection doors, a suitability certificate is required for the door. Area of application: Door width: min.: 1300 mm max.: 2200 mm Colour: ( ) silver-coloured Accessories: ( ) Integrated almost invisible flexible opening restrictor for E/R/ISM guide rails |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is infinitely variable adjustable (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |